## Slide 1: T.V.SURI AppaRao Assistant Professor Department of EECE GITAM Institute of Technology(GIT) Visakhapatnam-530045 Email: vtanakal@gitam.edu
UNIT-2 :Data Transmissions

## Slide 2: Syllabus
Unit I: Data communication, Data networking and the Internet: A communication model, data communications, networks, the Internet. Protocol Architecture: Need for protocol architecture, TCP/IP protocol architecture, OSI model, TCP/IP Vs OSI model.
Unit II: Data transmission: Concepts and terminology, analog and digital data transmission, transmission impairments, channel capacity. Transmission Media: Guided and unguided
Unit III: Signal encoding techniques: Digital data to digital signals, digital data to analog signals, analog data to digital signals, analog data to analog signals.
Unit IV: Digital Data Communication Techniques: Asynchronous and synchronous transmission, types of errors, error detection techniques, error correction techniques (single bit)
Data link control protocols: Flow control, error control, high level data link control (HDLC) protocol.
Unit V: Multiplexing: Frequency division multiplexing, characteristics, synchronous time division multiplexing, characteristics. statistical time division multiplexing, characteristics.
Text Book(s): 1 William Stallings, Data and Computer Communications, 8/e, Pearson Education., 2013.
References:
1. Fred Harshall, Data Communications, Computer Networks and Open systems,4/e, Pearson Education, 2005.
2. Behrouz A Forouzan, Data Communications and Networking, 4/e, McGraw Hill, 2012.

## Slide 3: DATA TRANSMISSION
Concepts and Terminology
Analog and Digital Data Transmission
Transmission Impairments
Channel Capacity
Transmission Media: Guided and unguided

## Slide 4: Introduction: . All the forms of information Eg : Voice, Data , Image, Video can be represented by EM signals . Electromagnetic (EM) signals in the form of analog or digital can be used to convey the information. . It is made up of a number of constituent frequencies. . An important parameter that characterizes the signal is Bandwidth. . Bandwidth is the width of the range of frequencies that comprises the signal. . Greater the bandwidth of the signal, greater is the information carrying capacity. . Major difficulty in designing a communications facility is Transmission Impairment.

## Slide 5
. The most significant impairments are :
(i) Attenuation
(ii) Attenuation Distortion
(iii) Delay Distortion
(iv) Various types of Noise
. Various types of Noise include,
(i) Thermal Noise
(ii) Intermodulation Noise
(iii) Crosstalk
(iv) Impulse Noise

## Slide 6
• For analog signals, transmission impairments introduce random effects that degrade the quality of the received
information and may affect intelligibility
. For digital signals, transmission impairments may cause bit errors at the receiver.
. The designer of a communications facility deals with 4 factors :
(i) Bandwidth of the signal
(ii) Data rate
(iii) Amount of noise and other impairments
(iv) Acceptable error rate

## Slide 7: . The successful transmission of data depends primarily on 2 factors : (i) Quality of signal being transmitted (ii) Characteristics of the transmission medium

## Slide 8: Concepts & Terminology : . In this we will see few terms and understand what they mean A - Transmission Terminology : . Data transmission occurs between transmitter and receiver over some transmission medium . Transmission medium can be classified as, (i) Guided – Waves are guided along a physical path (ii) Unguided - Waves are not guided along a physical path . Examples of guided media are Twisted pair , Coaxial cable, Optical fiber . Examples of Unguided media are propagation through air, vacuum and sea water

## Slide 9: . Direct Link : It refers to the transmission path between 2 devices in which signals propagate directly from transmitter to receiver with no intermediate devices in between them. . Point to Point : A guided transmission medium is point to point if it provides a direct link between 2 devices & those are the only 2 devices sharing the medium . Multi Point : In this, more than 2 devices share the same medium . A transmission medium may be, (i) Simplex (ii) Half- Duplex (iii) Full- Duplex

## Slide 10: Fig : Analog & Digital Waveforms

## Slide 11: .Time Domain – Viewed as a function of time, an EM signal can be either Analog or Digital . Analog signal – Varies in a smooth fashion over time No breaks / discontinuities in the signal . Digital Signal – Signal intensity maintains a constant level for one period of time & abruptly changes to another constant level. . Periodic signal – Same signal pattern repeats over time In mathematical form, a signal s(t) is periodic if and only if, s ( t + T ) = s(t) , - ∞ < t < + ∞ where, T = Period of the signal

## Slide 12: . The sine wave is the fundamental periodic signal . A general sine wave can be represented by 3 parameters : (i) Amplitude (A) (ii) Frequency (f) (iii) Phase (ø) . Peak Amplitude : Maximum value or strength of the signal over time. . Frequency : It is the rate ( in cycles/sec, or Hertz (Hz) at which the signal repeats ) . Time period (T) : Amount of time it takes for one repetition Therefore , T = 1 / f

## Slide 13: Fig : Examples of Periodic signals

## Slide 14: . Phase : It is a measure of the relative position in time within a single period of a signal . General sine wave pattern can be written as, . Wavelength : It is the distance occupied by a single cycle. . DC component : If a signal includes a component of Zero frequency, that component is a direct current (dc) or constant component It has frequency f = 0 & non-zero average amplitude

## Slide 15: Fig : Graphs that display the value of signal at a given point

## Slide 16: . Frequency Domain concept : An EM signal will be made up of many frequencies Examples :

## Slide 17: . Frequency Domain concept : Examples :

## Slide 18: Analog and Digital Data Transmission : . Data- Entities that convey meaning or information . Signals – Electric or Electromagnetic representations of data . Signalling – Physical propagation of the signal along a suitable medium . Transmission – Communication of the data by the propagation and processing of signals . Analog data take on continuous values in some interval Eg : Voice & Video are continuously varying patterns of intensity Data collected by sensors, such as temperature and pressure, are continuous valued . Digital data takes on discrete values Eg: Text, Integers

## Slide 19: . Most familiar example of analog data is Audio, which is in the form of acoustic sound waves . Frequency components of typical speech, 100 Hz - 7000 Hz . Another example of analog data is Video . To produce a picture on the screen, an electron beam scans across the surface of the screen from left to right and top to bottom

## Slide 20: Fig : Acoustic Spectrum of speech and music

## Slide 21: . For a black & white TV, the amount of illumination produced at any point is proportional to the intensity of the beam as it passes that point . At any instant of time, the beam takes an analog value of intensity to produce the desired brightness at that point on the screen . Therefore, as the beam scans, analog value changes and the video image is a time-varying analog signal

## Slide 22: Scanning Process : . At the end of each scan line, the beam is swept rapidly back to the left .This is known as Horizontal Retrace . When the beam reaches the bottom, it is swept rapidly back to the top . This is known as Vertical Retrace . The beam is turned off i.e; blanked out during retrace intervals . To achieve good resolution , the beam produces a total of 483 horizontal lines at a rate of 30 scans/sec . Practically, this rate will Produce Flicker. . To avoid this Flicker, new method of scanning is introduced known as Interlaced Scanning. . In this ,the total number of lines are divided into 2 fields, (i) Odd Field (ii) Even Field . The odd numbered scanned lines & even numbered scanned lines are scanned separately.

## Slide 23: . Odd Field : Scan from A to B . Even field : Scan from C to D . Therefore, the screen is refreshed 60 times/sec rather than 30 times/sec. . An example of digital data is Text and are transmitted in a binary fashion . These characters are represented by a sequence of bits . The most commonly used text code is the International Reference Alphabet (IRA) . Each character in this code is represented by a unique 7 bit pattern (128 characters can be represented) . The 8th bit is a parity bit used for Error detection

## Slide 24: Fig : Acoustic Spectrum of speech and music

## Slide 25: Analog & Digital Signals : . In a communications system, data are propagated from one point to another by means of EM signals . An analog signal is a continuously varying EM wave that can be propagated over a variety of media depending on the spectrum. Eg : Wire media – Twisted pair , Coaxial cable , Fiber optic cable Unguided media – Space propagation . A digital signal is a sequence of voltage pulses transmitted over a medium . Advantage of digital signaling over analog signaling is, (i) Economical (ii) Less susceptible to noise interference

## Slide 26: . Disadvantage of digital signaling over analog signaling is that digital signals suffer from more attenuation than analog signals Fig : Attenuation of Digital Signals . The figure shows a sequence of voltage pulses generated by a source using 2 voltage levels . Due to the attenuation, the pulses become rounder and smaller

## Slide 27: Data and Signals : . Analog data are a function of time & occupy a limited frequency spectrum . Digital data can be represented by digital signals, with a different voltage level for each of the 2 binary digits Fig: Analog Signaling of Analog and Digital Data

## Slide 28: . Digital data can be represented by analog signals by the use of Modem . Modem stands for Modulator- Demodulator . Modem converts a series of binary voltage pulses into an analog signal by encoding the digital data onto a carrier frequency . At the other end of the line, another modem demodulates the signal to recover the original data .

## Slide 29: Fig: Analog Signaling of Analog and Digital Data

## Slide 30: . In an operation similar to modem, analog data can be represented by digital signals . The device that performs this function for voice data is a Codec . Codec stands for Coder - Decoder . Codec takes an analog signal that directly represents the voice data & approximates that signal by a bit stream . At the receiving end, the bit stream is used to reconstruct the analog data .

## Slide 31: Analog and Digital Transmission : . Both analog and digital signals are transmitted on suitable transmission media . The way these signals are treated is a function of the transmission system . Analog transmission is a means of transmitting analog signals without regard to their content i . e ; the signal may represent analog data ( in terms of voice ) or digital data ( binary data pass through the modem ) . In both the cases, the analog signal gets attenuated . To achieve longer distances, transmission system introduces amplifiers that boost the energy in the signal . Unfortunately, the noise signal also gets amplified

## Slide 34: . For analog data such as voice , little distortion is tolerated and the data remain intelligible . For digital data, cascaded amplifiers will introduce errors . Digital transmission in contrast, assumes a binary content to the signal . Digital signal can be transmitted smaller distances without attenuation . To achieve greater distances, Repeaters are used . A repeater receives the digital signal, recovers the patterns of 1s & 0s and retransmits a new signal . Therefore, Attenuation is overcome. . The same technique may be applied for an analog signal if it is assumed that the signal carries digital data . At appropriately spaced points, the transmission system has repeaters . Repeater recovers the digital data from the analog signal and generates a new, clean analog signal . Therefore the noise is not cumulative.

## Slide 35: Telecommunication facilities have move to digital because of the following reasons, (i) Digital Technology : Because of LSI, VLSI , the cost is reduced and device has become more compact (ii) Data integrity : Integrity of data is achieved by using repeaters (iii) Capacity Utilization : Economical to build transmission links of very high bandwidth with optical fiber and this is achieved by digital ( Time division Multiplexing ) (iv) Security and Privacy : Using Encryption techniques this can be achieved (V) Integration : Economies of scale and convenience can be achieved by integrating voice, video and digital data

## Slide 36: Transmission Impairments : The most significant impairments are, (i) Attenuation & Attenuation distortion (ii) Delay Distortion (iii) Noise Attenuation : . The strength of a signal falls off with distance over any transmission medium . For guided media, attenuation varies exponentially and is expressed in decibels. . For unguided media, attenuation is a more complex function of the distance & the makeup of the atmosphere

## Slide 37: . Attenuation introduces 3 considerations for the transmission engineer, . First, a received signal must have sufficient strength so that the electronic circuitry in the receiver can detect the signal . Secondly, it must have a good SNR . Attenuation varies with frequency . First and second problems can be solved by attention to the signal strength and by using Repeaters . Third problem can be solved by Equalization . .

## Slide 38: Fig: Attenuation curve for a voice channel .

## Slide 39: . The figure shows the Attenuation Vs Frequency for a typical leased line . A 1 KHz tone of a given power level is applied to output & the power P1000 is taken at the output . Relative attenuation in dB is given as, . The frequency components a the upper end of the voice band are attenuated much more than that of lower frequencies. .Therefore, it results in a distortion in the received speech signal . The dashed line shows the effect of Equalization . Flattened response curve improves the quality of voice signals . Attenuation distortion can present less of a problem with digital signals. .

## Slide 40: Delay Distortion : . Delay Distortion occurs because the velocity of propagation of a signal through a guided medium varies with frequency . For a bandlimited signal, the velocity tends to be highest near the center frequency and fall off toward the two edges of the band . Therefore, various frequency components of a signal arrive at the receiver at different times resulting in phase difference between different frequencies . This effect is known as Delay Distortion as the received signal is distorted due to various delays experienced at its constituent frequencies

## Slide 41: Fig: Delay Distortion curve for a voice channel .

## Slide 42: . Attenuation introduces 3 considerations for the transmission engineer, . First, a received signal must have sufficient strength so that the electronic circuitry in the receiver can detect the signal . Secondly, it must have a good SNR . Attenuation varies with frequency . First and second problems can be solved by attention to the signal strength and by using Repeaters . Third problem can be solved by Equalization .

## Slide 43: Noise : . Undesired signals are referred to as Noise . Noise is the major limiting factor in communications systems reference . Noise is divided into 4 categories, (i) Thermal Noise (ii) Intermodulation Noise (iii) Crosstalk (iv) Impulse Noise . Thermal noise is due to thermal agitation of electrons . Thermal agitation of electrons is the random movement of free electrons in a conductor producing noise signals. . Thermal noise is a function of temperature

## Slide 44: . Thermal noise is uniformly distributed across the bandwidths, so it is referred to as White Noise . Thermal noise is significant for satellite communication as the received signal strength is less . The amount of Thermal noise to be found in a bandwidth of 1 Hz is given by, where, . Thermal noise power density at room temperature is 4 x 10-21 Hz or - 204 dBW/Hz

## Slide 45: . Noise is assumed to be independent of frequency N = KTB . N( in dBW ) = 10 log K + 10 log T + 10 log B = -228.6 dBW + 10 log T + 10 log B . Given a receiver with effective noise temperature of 294 K and 10 MHz bandwidth. Determine the thermal noise level at the receiver’s output ? . N = -228.6 dBW + 10 log ( 294 ) + 10 log (107 ) N = -228.6 + 24.7 + 70 N = -133.9 dBW

## Slide 46: . Intermodulation (IM) noise may occur when signals at different frequencies share the same transmission medium . The effect of IM noise is to produce signals at a frequency that is sum / difference or product of those frequencies. . IM noise is produced by nonlinearities in the transmitter , receiver ,transmission medium . Ideally these components are linear but in real time the output is more complex function of input . Excessive nonlinearity can be caused by component malfunction or from overload. . Cross talk may occur by electrical coupling between nearby twisted pairs, etc . Crosstalk can also occur when microwave antenna picks up unwanted signals . Typically, crosstalk is of the same order of magnitude or less than thermal noise . Impulse noise is non-continuous , consisting of irregular pulses or noise spikes of short duration and of relatively high amplitude

## Slide 47: . It occurs from a variety of causes such as electromagnetic disturbances ( eg: Lightning, faults and flaws in the communication system

## Slide 48: Fig: Effect of Noise on a Digital signal

## Slide 49: Channel Capacity : . Channel capacity is defined as the maximum rate at which the data can be transmitted over a given communication path, or channel , under given conditions. . Data Rate – The rate, in bits per second (bps) , at which data can be communicated . Bandwidth – The bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium expressed in cycles/sec, or Hertz . Noise – The average level of noise over the communications path . Error rate – The rate at which the error occurs , where an error is the reception of 1 when a 0 was transmitted or the reception of 0 when a 1 was transmitted

## Slide 50: Nyquist Bandwidth : . Consider the channel as Noise free . Therefore, the limitation of data rate is nothing but the bandwidth of the signal . A formulation of this limitation, due to Nyquist states that, If the rate of signal transmission is 2B, then a signal with frequencies no greater than B is sufficient to carry the signal rate or vice versa. . This limitation is due to the effect of ISI . ISI stands for Inter Symbol Interference .This is useful in the development of digital-to-analog encoding schemes . If the signals to be transmitted are binary , then the data rate that can be supported by B Hz is 2B bps . Binary supports 2 voltage levels . If 4 possible voltage levels are used as signals ,then each signal element can represent 2 bits

## Slide 51: . With multi level signaling, the Nyquist formulation is, C = 2B log2 M where, M = Number of discrete signal or voltage levels B = Bandwidth C = Nyquist capacity . Therefore, for a given bandwidth the data rate can be increased by increasing the number of different signal elements . But doing this , there will be an increased burden on the receiver . Consider a voice channel being used for a modem to transmit digital data. Given Bandwidth is 3.1 KHz & M =8. Determine the Channel capacity ?

## Slide 52: C = 2B log2 M C = 2 x 3100 x log2 8 C = 2 x 3100 x log2 23 C = 2 x 3100 x 3 x log2 2 C = 2 x 3100 x 3 x 1 C = 18600 bps (or) 18.6 Kbps Shannon Capacity Formula : . Nyquist’s formula is based on noise free environment. So, doubling the bandwidth doubles the data rate . The presence of noise can corrupt one or more bits . If the data rate is increased, the bits become shorter and therefore more bits are affected by noise . The above diagram represents the scenario

## Slide 53: . All of these factors are included in the formula developed by Shannon . Higher the data rate, the more the noise . Therefore, for a given level of noise, a greater signal strength will improve the ability to receive the data correctly in the presence of noise . The key parameter that describes this is, Signal-to-Noise ratio ( SNR) . SNR is defined as the ratio of Signal power to the Noise power . SNR (in dB) , can be represented as , . Higher the SNR, better is the quality of the signal

## Slide 54: . All of these factors are included in the formula developed by Shannon . Higher the data rate, the more the noise . Therefore, for a given level of noise, a greater signal strength will improve the ability to receive the data correctly in the presence of noise . The key parameter that describes this is, Signal-to-Noise ratio ( SNR) . SNR is defined as the ratio of Signal power to the Noise power . SNR (in dB) , can be represented as , . Higher the SNR, better is the quality of the signal

## Slide 55: . The maximum channel capacity (in bps) is given as, Where, C = Channel capacity ( in bits per sec (or) bps) B = Bandwidth SNR = Signal to Noise ratio . By using this formula, we can get theoretical maximum values, but practically the values will be lesser than this . The reason is, this formula includes only thermal noise i.e ; White Noise Attenuation distortion, delay distortion, impulse noise are not included

## Slide 56: . Consider an example which relates Nyquist and Shannon relation . Given the spectrum of a channel is in between 3 MHz and 4 MHz & SNR = 24 dB Therefore, Bandwidth = 4 - 3 = 1 MHz SNR = 24 dB 10 log SNR = 24 log SNR = 24/10 = 2.4 SNR = 10 2.4 SNR = 251.188

## Slide 57: Using Shannon’s formula, C = B log 2 ( 1 + SNR) C = 10 6 x log 2 ( 1 + 251.188 ) C = 10 6 x log 2 (252.188 ) C = 10 6 x 7.9783 C (Approx.) = 8 Mbps Using Nyquist’s formula, C = 2 x 10 6 log2 M 8 x 10 6 = 2 x 10 6 log2 M log2 M = 4 M = 2 4 = 16

## Slide 58: Expression Eb / No : . The parameter Eb / No is a quality measure for determining the digital communication system performance . This parameter is used to measure digital data rates and error rates . Eb / No parameter is the ratio of signal energy per bit to noise power density per Hz . Consider a signal that contains binary digital data transmitted at a rate R . The energy per bit in a signal is given as, Eb = S Tb where, S = Signal power Tb = Time required to send one bit

## Slide 59: . The data rate R is , R = 1/ Tb . Eb / No is given as,

## Slide 60: . For BPSK, Eb / No = 8.4 dB is required for a bit error rate of 10- 4 . If the effective noise temperature is 290 K and the data rate is 2.4 Kbps . Determine the received signal level ? 8.4 = S (in dBW) – 10 log 2400 + 228.6 – 10 log 290 8.4 = S (in dBW) – 33.802+ 228.6 – 24.623 S (in dBW) = -161.774 . Eb / No can be related to SNR as, Where , No = Noise power density ( in Watts / Hz)

## Slide 61: . Therefore, Noise in a signal with bandwidth B is N = NoB . After substituting, . Eb / No is related to spectral efficiency as, . Equating R with C,

## Slide 62: . Determine the minimum Eb / No required to achieve a spectral efficiency of 6bps/Hz ? Eb / No = 1/6 ( 2 6 - 1) = 10.5 Eb / No = 10 log 10.5 =10.212 dB

## Slide 63: Guided & Unguided Transmission Media : . Transmission media that are used to convey the information may be classified as, (i) Guided media – Uses Twisted pair, coaxial cable or optical fiber (ii) Unguided media – Uses an antenna for transmitting through air, vacuum, or water . Number of design factors relating to the transmission medium and the signal determine the data rate and distance: (i) Bandwidth – Greater the bandwidth of a signal, the higher the data rate that can be achieved ( Assuming that other factors are constant ) (ii) Transmission Impairments – Impairments such as attenuation limit the distance Eg: Twisted pair > Coaxial cable > Optical fiber (iii) Interference - In Guided media , it can be caused by emanations from nearby cables In Un-guided media, it can be caused from overlapping frequency bands

## Slide 64: . Number of Receivers – Guided medium can be used to construct a point to point link or a shared link with multiple attachments. Each attachment introduces some attenuation limiting the distance and/or data rate.

## Slide 65: . Guided Transmission Media : . In this, the transmission capacity ( in terms of either Data rate or Bandwidth ) depends critically on the distance & the medium ( Point - to - Point or Multi point) . The three guided media commonly used for transmission are, (i) Twisted pair (ii) Coaxial cable (iii) Optical fiber

## Slide 66: Fig : Electromagnetic (EM) Spectrum for Telecommunications

## Slide 67: Fig : Point-to-Point transmission characteristics of Guided media

## Slide 68: Fig : Twisted Pair Fig : Coaxial cable

## Slide 69: Fig : Optical Fiber

## Slide 70: Twisted Pair : . It is the least expensive and mostly used guided transmission media . It consists of 2 insulated copper wires arranged in a regular spiral pattern and this wire pair acts as a single communication link . Over long distance, cables may contain hundreds of pairs . The twisting tends to decrease the crosstalk interference between adjacent pairs in a cable . Over long distance links, the twist length varies from 5-15 cm & the wires in a pair have thickness from 0.4- 0.9mm

## Slide 71: Applications : . It is used in the telephone network and is the workhorse for communications within buildings . In the telephone system, individual residential telephone sets are connected to the local telephone exchange or end office by this twisted pair and are referred to as Subscriber loops . Within an office building, each telephone is connected to the twisted pair which goes to the in-house PBX ( Private Branch Exchange) and are used to support voice traffic ( Using Analog signaling ) . By using a Modem, these can handle digital data traffic at modest data rates . It can be commonly used within a building for LAN’s ( Local Area Network ) supporting PC’s ( Personal Computer) . Twisted pair is less expensive when compared with other guided transmission media.

## Slide 72: Transmission characteristics : . Twisted pair is used to transmit both analog and digital data transmission . For Analog signals – Amplifiers are used . For Digital signals – Repeaters are used . Compared to the other guided transmission media , Twisted pair is limited in distance, bandwidth and data rate . Impulse noise easily intrudes into twisted pair . It is quite susceptible to interference and noise because of its easy coupling with EM (Electro-Magnetic) fields . Shielding the wire with metallic braid or sheathing reduces interference . Twisting of the wire reduces low-frequency interference. . Use of different twist lengths in adjacent pairs reduces crosstalk

## Slide 73: Fig : Attenuation of typical Guided media

## Slide 74: Unshielded and Shielded Twisted pair : . Twisted pair is in 2 variants, (i) Shielded Twisted pair (STP) (ii) Unshielded Twisted pair (UTP) . UTP is an ordinary telephone wire. It is less expensive of all the transmission media commonly used for LAN’s and easy to work with and easy to install . UTP is subject to external EM interference . It can be improved by proper shielding with a metallic braid or sheathing which reduces the interference . STP provides better performance but is more expensive & is more expensive to work with than UTP

## Slide 75: Category 3 & Category 5 UTP : . In the year 1991, EIA ( Electronic Industries Association ) published standard EIA-568, Commercial Building Telecommunication Cabling Standard. . It specifies the use of UTP and STP for in-building data applications . EIA-568-A recognizes 3 categories of UTP cabling as, (i) Category 3 – UTP cables & associated hardware whose transmission characteristics are specified upto 16 MHz (ii) Category 4 - UTP cables & associated hardware whose transmission characteristics are specified upto 20 MHz (iii) Category 5 - UTP cables & associated hardware whose transmission characteristics are specified upto 100 MHz . Out of these Category 3 & 5 found LAN applications . Over limited distance , Category 3- Up to 16 Mbps, Category 5 – Up to 100Mbps . Key difference between Category 3 & 5 is the number of twists in the cable per unit distance

## Slide 76: Fig : Comparison of STP & UTP

## Slide 77: Category 3 & Category 5 UTP : . For a guided media, attenuation is generally exponential and expressed as a constant no. of decibels per unit distance . Near end cross talk occurs when there is coupling of the signal from one pair of conductors to another pair . These conductors may be the metal pins in a connector or wire pairs in a cable

## Slide 78: Coaxial Cable : . It operates over a wide range of frequencies . It consists of a hollow outer cylindrical conductor that surrounds a single inner wire conductor Inner conductor – Regularly spaced insulating rings or a solid dielectric material Outer conductor – Covered with a jacket or shield . A single coaxial cable has a diameter of 1 - 2.5 cm . It can be used over longer distances and support more stations Applications: Used in, . Television distribution . Long-distance telephone distribution . Short-run computer system links . LAN’s ( Local Area Networks )

## Slide 79: Coaxial Cable : . Coaxial cable is an important part of the long distance telephone network . Now-a-days it faces increasing competition from optical fiber, terrestrial microwave and satellite . Using FDM ( Frequency Division Multiplexing ), a coaxial cable can carry 10,000 voice channels simultaneously . Coaxial cable is commonly used for short range connections between devices . Using digital signaling, coaxial cable can provide high speed I/O channels on computer systems Transmission Characteristics : . It can transmit both analog & digital signals . Coaxial cable works better than twisted pair as it operates at higher frequencies . It is much less susceptible to interference & crosstalk due to its shielded, concentric construction . The main constraints on its performance are Attenuation, Thermal Noise and Inter-modulation (IM) Noise

## Slide 80: Optical Fiber : . An optical fiber is a thin, flexible medium capable of guiding an optical ray. . Glass , Plastic can be used to make optical fibers . Less losses are obtained using fibers of Ultrapure fused Silica but it is difficult to manufacture . Higher-loss multicomponent glass fibers are more economical and provide good performance . Plastic fibers are even less costly and is used for short-haul links . Optical fiber cable has a cylindrical shape and consists of 3 concentric sections, They are, (i) Core (ii) Cladding (iii) Jacket

## Slide 81: Fig : Optical Fiber

## Slide 82: . Core – It is the inner most section and consists of one or more very thin strands, or fibers , made of glass or plastic. It has a diameter of 8-50 µm. . Cladding – Optical fiber is surrounded by cladding (Glass/Plastic coating that has different optical properties from that of core ). It has a diameter of 125 µm. . Jacket – It is the outermost layer surrounding one or a bundle of cladded fibers to protect against moisture, abrasion, crushing, etc Applications : . Greater Capacity – The potential bandwidth and hence high data rate of optical fiber is immense ( Data rates of hundreds of Gbps over tens of kilometers is achieved ) . Smaller Size & Lighter weight – Are considerably thinner compared with others . Attenuation – Significantly lower than coaxial cable and twisted pair

## Slide 83: . Electromagnetic (EM) Isolation – Not affected by external EM fields. Therefore, the system is not vulnerable to interference, impulse noise or crosstalk. Fibers don’t radiate energy, so there is little interference with other equipment & there is a high degree of security from eavesdropping . Greater Repeater spacing - Fewer repeaters mean lower cost and less error. Repeater spacing is more in optical fiber when compared with twisted pair and coaxial cable 5 categories of applications have become popular for optical fiber, (i) Long- haul trunks (ii) Metropolitan trunks (iii) Rural exchange trunks

## Slide 84: (iv) Subscriber loops (v) Local Area Networks (LAN’s) . Long- haul Trunks – Long-haul fiber transmission has become increasingly common in the telephone network. These systems compete economically with microwave. Undersea optical fibers are also used more. . Metropolitan Trunks – Most facilities are installed in under ground conditions and are repeater-less joining a telephone exchange in a metropolitan area . Rural Exchange Trunks – Have circuit lengths ranging from 40-160 Km and link towns and villages. Technology used in these applications competes with microwave facilities . Subscriber loop circuits – Are fibers that run directly from the central exchange to a subscriber. These facilities are beginning to displace twisted pair and coaxial cable links as telephone networks now are capable of not only handling voice, data but also image and video

## Slide 85: . Local Area Networks (LAN’s) - Standards have been developed and have total capacity of 100 Mbps to 10Gbps can support more number of stations or offices Transmission characteristics : . Optical fiber transmits a signal-encoded beam of light by means of Total Internal Reflection (TIR) . TIR can occur in any transparent medium that has a higher index of refraction than the surrounding medium . Optical fiber acts as a waveguide for frequencies in the range of 1014 to 1015 Hz . Rays at shallow angles are reflected and propagated along the fiber and other rays are absorbed by the surrounding material. This is referred to as Step index multi mode . Graded index mode is possible by varying the refractive index. . Light in the core curves helically because of graded index, reducing its travel distance

## Slide 86: Fig : Optical fiber Transmission modes